## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Past Year’s Exam Paper
AY2017/18 Semester 2

## Slide 2: Download paper from CS2100 “Exams” web page: https://www.comp.nus.edu.sg/~cs2100/3_ca/exams.html

## Slide 3: 1(a)
#include <stdio.h>
typedef struct {
int val;
char ch[2];
} rec_t;
int main(void) {
rec_t st[2] = {{11,{'A','B'}}, {22,{'C','D'}}};
process1(&st[1]);
process2(st[0]);
printf("%d %c\n", st[0].val, st[0].ch[0]);
printf("%d %c\n", st[1].val, st[1].ch[1]);
return 0;
}
void process1(rec_t *para) {
para->val = 33;
para->ch[0] += ('a' - 'A') + 1;
para->ch[1] += ('a' - 'A') + 2;
}
void process2(rec_t para) {
para.val = 44;
para.ch[0] += ('a' - 'A') + 3;
para.ch[1] += ('a' - 'A') + 4;
}

## Slide 4: 1(a)
#include <stdio.h>
typedef struct {
int val;
char ch[2];
} rec_t;
int main(void) {
rec_t st[2] = {{11,{'A','B'}}, {22,{'C','D'}}};
process1(&st[1]);
process2(st[0]);
printf("%d %c\n", st[0].val, st[0].ch[0]);
printf("%d %c\n", st[1].val, st[1].ch[1]);
return 0;
}
void process1(rec_t *para) {
para->val = 33;
para->ch[0] += ('a' - 'A') + 1;
para->ch[1] += ('a' - 'A') + 2;
}
void process2(rec_t para) {
para.val = 44;
para.ch[0] += ('a' - 'A') + 3;
para.ch[1] += ('a' - 'A') + 4;
}
st
11
'A'
'B'
st0
22
'C'
'D'
st1
para
33
'd'
'f'
para
11
'A'
'B'
44
'd'
'f'
11 A
33 f
Notes: For the first rec_t, which was copied into process2, inside the function, the copy value was changed into 44, but the actual value didn’t change. The characters in the string copy changed as well, but the original string didn’t change.
For the second rec_t, which was passed into process1 as a pointer, the actual value was changed into 33. The characters in the original string were changed as well.

## Slide 5: 1(b)
Given the hexadecimal representation in IEEE 754 single-precision floating-point number system:
4 2 F 6 4 0 0 0
What is the decimal value it represents?

## Slide 6: 1(b)
Given the hexadecimal representation in IEEE 754 single-precision floating-point number system:
4 2 F 6 4 0 0 0
What is the decimal value it represents?
0100 0010 1111 0110 0100 0000 0000 0000
10000101 = 133 – 127 = 6
1.111011001  26 = 1111011.0012 = 132.125
Notes: Remember in IEEE standard conversion, the exponent applies to the mantissa as it is portrayed in the number sample, not after conversion. Therefore, if the final answer is too complicated, then chances are that it is wrong and must redo.

## Slide 7: 1(c)
Given the logic circuit below:
A
B
F
What is F?
What is the circuit propagation delay if the propagation delay of a NAND gate with fan-in of n is nt?

## Slide 8: 1(c)
Given the logic circuit below:
A
B
F
What is F?
What is the circuit propagation delay if the propagation delay of a NAND gate with fan-in of n is nt?
1
(Faster by truth table or trace AB=00,01,10,11.)
A'+B
B'+A
AB
(AB)'
9t

## Slide 9: 2.
A sequential circuit goes through the following states, whose state values are shown in decimal:
0
1
3
2
6
15
13
4
5
7
12
The states are represented by 4-bit values ABCD. Implement the sequential circuit using D flip-flops for A and B, a T flip-flop for C, and a JK flip-flop for D.
Write out the simplified SOP expressions for all the flip-flop inputs.
Implement your circuit according to your simplified SOP expressions obtained in part (a). Complete the given state diagram by indicating the next state for each of the five unused states.

## Slide 10: 2.
0
1
3
2
6
15
13
4
5
7
12
Current stateX |  |  |  | Next state |  |  |  |  |  | 
A | B | C | D | A+ | B+ | C+ | D+ | TC | JD | KD
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | X
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | X
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | X
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | X | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | X | X | X | X | X | X | X
1 | 0 | 0 | 1 | X | X | X | X | X | X | X
1 | 0 | 1 | 0 | X | X | X | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X | X | X | X
1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | X
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | X | 0
1 | 1 | 1 | 0 | X | X | X | X | X | X | X
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | X | 1
DA
C
B
A
D
0
0
0
0
1
0
0
0
1
1
0
X
X
X
X
X
DB
C
B
A
D
0
0
0
1
1
1
1
1
1
1
0
X
X
X
X
X
TC
C
B
A
D
0
1
0
0
0
0
1
0
0
1
1
X
X
X
X
X
JD
C
B
A
D
1
X
X
0
0
X
X
1
1
X
X
X
X
X
X
X
KD
C
B
A
D
X
0
1
X
X
1
0
X
X
0
1
X
X
X
X
X
DA = A∙C' + B∙C'∙D'
DB = A'∙B + C∙D' + B∙C'
or A'∙B + C∙D' + A∙C'
TC = A∙D + B∙C∙D + B'∙C'∙D
JD = A + B∙C + B'∙C'
KD = A∙C + B'∙C + A'∙B∙C'

## Slide 11: 2.
0
1
3
2
6
15
13
4
5
7
12
Current stateX |  |  |  | Next state |  |  |  |  |  | 
A | B | C | D | A+ | B+ | C+ | D+ | TC | JD | KD
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | X
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | X
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | X
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | X | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | X | X | X | X | X | X | X
1 | 0 | 0 | 1 | X | X | X | X | X | X | X
1 | 0 | 1 | 0 | X | X | X | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X | X | X | X
1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | X
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | X | 0
1 | 1 | 1 | 0 | X | X | X | X | X | X | X
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | X | 1
DA
C
B
A
D
0
0
0
0
1
0
0
0
1
1
0
X
X
X
X
X
DB
C
B
A
D
0
0
0
1
1
1
1
1
1
1
0
X
X
X
X
X
TC
C
B
A
D
0
1
0
0
0
0
1
0
0
1
1
X
X
X
X
X
JD
C
B
A
D
1
X
X
0
0
X
X
1
1
X
X
X
X
X
X
X
KD
C
B
A
D
X
0
1
X
X
1
0
X
X
0
1
X
X
X
X
X
DA = A∙C' + B∙C'∙D'
DB = A'∙B + C∙D' + B∙C'
or A'∙B + C∙D' + A∙C'
TC = A∙D + B∙C∙D + B'∙C'∙D
JD = A + B∙C + B'∙C'
KD = A∙C + B'∙C + A'∙B∙C'
1
1
0
0
0
0,1
0,1
1
0
1
0
0
1
1
0
1
1
1
1
1
0
0
1
1
1
0
1
1
0
1
1
1
1
1
0

## Slide 12: 2.
Current stateX |  |  |  | Next state |  |  |  |  |  | 
A | B | C | D | A+ | B+ | C+ | D+ | TC | JD | KD
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | X
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | X | 0
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | X
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | X
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | X | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | X
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | X | 0
1 | 0 | 0 | 0 | X | X | X | X | X | X | X
1 | 0 | 0 | 1 | X | X | X | X | X | X | X
1 | 0 | 1 | 0 | X | X | X | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X | X | X | X
1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | X
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | X | 0
1 | 1 | 1 | 0 | X | X | X | X | X | X | X
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | X | 1
1
1
0
0
0
0,1
0,1
1
0
1
0
0
1
1
0
1
1
1
1
1
0
0
1
1
1
0
1
1
0
1
1
1
1
1
0
0
1
3
2
6
15
13
4
5
7
12
8
9
10
11
14
There are two sets of answers, where states 8 and 9 may transit to different states.
Set 1: 8  9; 9  11
(Correspond to DB = A'∙B + C∙D' + B∙C’)
Set 2: 8  13; 9  15
(Correspond to DB = A'∙B + C∙D' + A∙C')

## Slide 13: 3(a)
Given the following circuit, what is F?
0
1
1×2
DEC
In
EN
A
B
A
A
B
F
S1
S0
I1
Io
I2
I3
4:1
MUX

## Slide 14: 3(a)
Given the following circuit, what is F?
0
1
1×2
DEC
In
EN
A
B
A
A
B
F
S1
S0
I1
Io
I2
I3
4:1
MUX
A | B | F
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
1
1
F = A

## Slide 15: 3(b)
Given G(A,B,C,D) = PM(1, 2, 6, 8, 9, 11, 13), implement G using a single 8:1 multiplexer without any additional logic gates. Complemented literals are not available.

## Slide 16: 3(b)
Given G(A,B,C,D) = PM(1, 2, 6, 8, 9, 11, 13), implement G using a single 8:1 multiplexer without any additional logic gates. Complemented literals are not available.
A | B | C | D | G
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
G
0
0
1
2
3
4
5
6
7
1
2
8:1
MUX
A C D
1
B
0
1
B
0
1
B

## Slide 17: 3(c)
Given H(A,B,C,D) = Sm(12, 13), implement H using a single 24 active high output decoder with 1-enable without any additional logic gates. Complemented literals are not available.
24
DEC
EN
S1
S0
0
1
2
3

## Slide 18: 3(c)
Given H(A,B,C,D) = Sm(12, 13), implement H using a single 24 active high output decoder with 1-enable without any additional logic gates. Complemented literals are not available.
24
DEC
EN
S1
S0
0
1
2
3
H = m12 + m13 = A∙B∙C'∙D' + A∙B∙C'∙D = A∙B∙C'
Many possible answers
A
B
C
H

## Slide 19: 3(d)
The BCD code values for the ten decimal digits are given below:
Digit: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
Given two decimal digits A and B, represented by their BCD codes A3A2A1A0 and B3B2B1B0, implement a circuit without using any logic gates to calculate the BCD code of the 3-digit output of
(51A) + (20  (B%2)), where % is the modulo operator.
Name the outputs F11F10F9F8F7F6F5F4F3F2F1F0.

## Slide 20: 3(d)
Given two decimal digits A and B, calculate the BCD code of the 3-digit output of
(51A) + (20  (B%2)).
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1

## Slide 21: 3(d)
Given two decimal digits A and B, calculate the BCD code of the 3-digit output of
(51A) + (20  (B%2)).
A |  |  |  | 51A |  |  |  |  |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1
A3 A2 A1 A0
B3 B2 B1 B0
F11 F10 F9 F8 F7 F6 F5 F4 F3 F2 F1 F0
0

## Slide 22: 4(a)
Suppose MIPS instructions in R-format must use the following five opcodes (in decimal): 0, 1, 16, 17 and 32, what is the maximum total number of instructions that can be supported in MIPS?

## Slide 23: 4(a)
Suppose MIPS instructions in R-format must use the following five opcodes (in decimal): 0, 1, 16, 17 and 32, what is the maximum total number of instructions that can be supported in MIPS?
Non-R-format = (26 – 5)
R-format = (5  26)
(26 – 5) + (5  26) = 59 + (5  64) = 59 + 320 = 379

## Slide 24: 4(b)
A stuck-at-0 fault occurs at bit 6 of every MIPS instruction. Devise a simple test using a MIPS instruction to discover this error. Explain your test.

## Slide 25: 4(b)
A stuck-at-0 fault occurs at bit 6 of every MIPS instruction. Devise a simple test using a MIPS instruction to discover this error. Explain your test.
Example: addi $t0, $zero, 64
opcode
rs
rt
immediate
6 5 4 3 2 1 0
15
64 = 00000000010000002
This is supposed to put the value 64 in $t0. However, due to the stuck-at-0 error at bit 6, the value in $t0 will be zero.
Other answers possible.

## Slide 26: 4(c)
Suppose the stuck-at-0 fault occurs at the ALUSrc control signal. Assuming $t0 and $t1 contain 12 and 34, and we are to use lw $t1, 0($t0) to discover the error. Describe what other preparation work needs to be done.

## Slide 27: 4(c)
Suppose the stuck-at-0 fault occurs at the ALUSrc control signal. Assuming $t0 and $t1 contain 12 and 34, and we are to use lw $t1, 0($t0) to discover the error. Describe what other preparation work needs to be done.
If the instruction is carried out correctly, lw $t1, 0($t0) would have loaded the value at address 12 into $t1.
With stuck-at-0 fault at ALUSrc, the instruction would have loaded the value at address 46 into $t1 instead.
Hence, we could first load different values in addresses 12 and 46 before using the test.

## Slide 28: 4(d)
The table below shows the ALUcontrol signal of the datapath.
Opcode | ALUop | Inst op | Funct | ALU action | ALU control
lw | 00 | load word | xxxxxx | add | 0010
sw | 00 | store word | xxxxxx | add | 0010
beq | 01 | branch equal | xxxxxx | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
R-type | 10 | subtract | 100010 | subtract | 0110
R-type | 10 | AND | 100100 | AND | 0000
R-type | 10 | OR | 100101 | OR | 0001
R-type | 10 | set on less than | 101010 | set on less than | 0111
You want to add the bne instruction into the datapath. Write out the ALUop for bne and how you can determine whether the bne results in the branch to be taken.

## Slide 29: 4(d)
You want to add the bne instruction into the datapath. Write out the ALUop for bne and how you can determine whether the bne results in the branch to be taken.
Since ALUop code 11 is not used, we may use it for bne.
Hence, branch taken = ALUop1 AND ALUop2 AND !(isZero)
where (isZero) is the output from the ALU.
or,
Use ALUop code 01 (same as beq).
Hence, branch taken = !ALUop1 AND ALUop2 AND !(isZero)
where (isZero) is the output from the ALU,
or branch taken = Branch AND !(isZero).
Other justified answers are possible.

## Slide 30: 5.
A and B are integer arrays whose base addresses are in $s0 and $s1. The arrays are of the same size n (number of elements).
$s2 contains the value n.
.data
A: .word 11, 9, 31, 2, 9, 1, 6, 10
B: .word 3, 7, 2, 12, 11, 41, 19, 35
n: .word 8
.text
main: la $s0, A # $s0 is the base address of array A
la $s1, B # $s1 is the base address of array B
la $t0, n # $t0 is the addr of n (size of array)
# $s2 is the content of n
beq $s2, $zero, End # Address: 0x0040003c
addi $t8, $s2, -1
sll $t8, $t8, 2
Loop: add $t0, $s0, $t8
add $t1, $s1, $t8
lw $t2, 0($t0)
lw $t3, 0($t1)
andi $t4, $t3, 3
addi $t4, $t4, -3
beq $t4, $zero, A1
add $t2, $t2, $t3
j A2
A1: addi $t2, $t2, 1
A2: sw $t2, 0($t0)
addi $t8, $t8, -8
slt $t7, $t8, $zero
beq $t7, $zero, Loop
End: li $v0, 10 # system call code for exit
syscall

## Slide 31: 5(a)
Fill in the missing instruction.
.data
A: .word 11, 9, 31, 2, 9, 1, 6, 10
B: .word 3, 7, 2, 12, 11, 41, 19, 35
n: .word 8
.text
main: la $s0, A # $s0 is the base address of array A
la $s1, B # $s1 is the base address of array B
la $t0, n # $t0 is the addr of n (size of array)
# $s2 is the content of n

## Slide 32: 5(a)
Fill in the missing instruction.
.data
A: .word 11, 9, 31, 2, 9, 1, 6, 10
B: .word 3, 7, 2, 12, 11, 41, 19, 35
n: .word 8
.text
main: la $s0, A # $s0 is the base address of array A
la $s1, B # $s1 is the base address of array B
la $t0, n # $t0 is the addr of n (size of array)
# $s2 is the content of n
lw $s2, 0($t0)

## Slide 33: 5(b,c)
Fill in the value of array A after the execution of the code.
Write an equivalent C code.
$s0 = addr. of array A; $s1 = addr. of array B; $s2 = n (size of array)
beq $s2, $zero, End # Address: 0x0040003c
addi $t8, $s2, -1
sll $t8, $t8, 2
Loop: add $t0, $s0, $t8
add $t1, $s1, $t8
lw $t2, 0($t0)
lw $t3, 0($t1)
andi $t4, $t3, 3
addi $t4, $t4, -3
beq $t4, $zero, A1
add $t2, $t2, $t3
j A2
A1: addi $t2, $t2, 1
A2: sw $t2, 0($t0)
addi $t8, $t8, -8
slt $t7, $t8, $zero
beq $t7, $zero, Loop
End:
A = {11, 9, 31, 2, 9, 1, 6, 10}
B = { 3, 7, 2, 12, 11, 41, 19, 35}
What does the code do?

## Slide 34: 5(b,c)
beq $s2, $zero, End # Address: 0x0040003c
addi $t8, $s2, -1
sll $t8, $t8, 2
Loop: add $t0, $s0, $t8
add $t1, $s1, $t8
lw $t2, 0($t0)
lw $t3, 0($t1)
andi $t4, $t3, 3
addi $t4, $t4, -3
beq $t4, $zero, A1
add $t2, $t2, $t3
j A2
A1: addi $t2, $t2, 1
A2: sw $t2, 0($t0)
addi $t8, $t8, -8
slt $t7, $t8, $zero
beq $t7, $zero, Loop
End:
Fill in the value of array A after the execution of the code.
Write an equivalent C code.
$s0 = addr. of array A; $s1 = addr. of array B; $s2 = n (size of array)
A = {11, 9, 31, 2, 9, 1, 6, 10}
B = { 3, 7, 2, 12, 11, 41, 19, 35}
int i;
for (i=n-1; i>=0; i-=2) {
if (B[i]%4 == 3)
A[i] = A[i] + 1;
else
A[i] = A[i] + B[i];
}
A = {11, 10, 31, 14, 9, 42, 6, 11}
No change

## Slide 35: 5(d-f)
Give the instruction encoding in hexadecimal for the following 3 instructions:
beq $s2, $zero, End # Address: 0x0040003c
addi $t8, $s2, -1
sll $t8, $t8, 2
Loop: add $t0, $s0, $t8
add $t1, $s1, $t8
lw $t2, 0($t0)
lw $t3, 0($t1)
andi $t4, $t3, 3
addi $t4, $t4, -3
beq $t4, $zero, A1
add $t2, $t2, $t3
j A2
A1: addi $t2, $t2, 1
A2: sw $t2, 0($t0)
addi $t8, $t8, -8
slt $t7, $t8, $zero
beq $t7, $zero, Loop
End:

## Slide 36: 5(d-f)
beq $s2, $zero, End # Address: 0x0040003c
addi $t8, $s2, -1
sll $t8, $t8, 2
Loop: add $t0, $s0, $t8
add $t1, $s1, $t8
lw $t2, 0($t0)
lw $t3, 0($t1)
andi $t4, $t3, 3
addi $t4, $t4, -3
beq $t4, $zero, A1
add $t2, $t2, $t3
j A2
A1: addi $t2, $t2, 1
A2: sw $t2, 0($t0)
addi $t8, $t8, -8
slt $t7, $t8, $zero
beq $t7, $zero, Loop
End:
Give the instruction encoding in hexadecimal for the following 3 instructions:
$t8 = $24
sll: 000000 00000 11000 11000 00010 000000
0 0 1 8 c 0 8 0
Addr. of sw at A2: 0x0040003c + (134)
= 0x0040003c + 0x34 = 0x00400070
0000 0000 0100 0000 0000 0000 0111 0000
000010 00000100000000000000011100
0 8 1 0 0 0 0 1 c
$t7 = $15; $t8 = $24
000000 11000 00000 01111 00000 101010
0 3 0 0 7 8 2 a

## Slide 37: 6.
Pipelining.
Covered in tutorial #10 question 3.

## Slide 38: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped data cache: 128 words, 4-word blocks, 4-byte words.
Arrays A and B at addresses 0x10001000 and 0x1003F100.
(a) How many bits are there in the index field? In the byte offset field?
Which index is A[1023] mapped to?
Which index is B[1023] mapped to?

## Slide 39: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped data cache: 128 words, 4-word blocks, 4-byte words.
Arrays A and B at addresses 0x10001000 and 0x1003F100.
(a) How many bits are there in the index field? In the byte offset field?
Which index is A[1023] mapped to?
Which index is B[1023] mapped to?
Number of blocks = 128/4 = 32 = 25
Number of bytes per block = 16 = 24
5
4
A[0] at 0x10001000; A[1024] at 0x10002000
A[1023] at 0x10001FFC  …1111 1111 1100  Index 31
B[0] at 0x1003F100; B[1024] at 0x10040100
B[1023] at 0x100400FC  …0000 1111 1100  Index 15

## Slide 40: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped data cache: 128 words, 4-word blocks, 4-byte words.
Arrays A and B at addresses 0x10001000 and 0x1003F100.
(c) How many memory accesses in total are made for array A? For array B?
(d) What is the cache hit rate for array A? For array B?

## Slide 41: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped data cache: 128 words, 4-word blocks, 4-byte words.
Arrays A and B at addresses 0x10001000 and 0x1003F100.
(c) How many memory accesses in total are made for array A? For array B?
(d) What is the cache hit rate for array A? For array B?
512 elements for each array are accessed:
[1023], [1021], …, [3], [1].
Array A: 1024 accesses (1 read and 1 write per element)
Array B: 512 accesses
Array A: 256 misses, 768 hits; hit rate = 75%
Array B: 256 misses, 256 hits; hit rate = 50%

## Slide 42: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped instruction cache: 16 words, 2-instruction blocks.
First instruction (beq) at memory address 0x0040003c.
Assuming beq instruction at Inst10 always branches to A1.
(e) How many cache hits and misses are there?
beq $s2, $zero, End # Inst1
addi $t8, $s2, -1 # Inst2
sll $t8, $t8, 2 # Inst3
Loop: add $t0, $s0, $t8 # Inst4
add $t1, $s1, $t8 # Inst5
lw $t2, 0($t0) # Inst6
lw $t3, 0($t1) # Inst7
andi $t4, $t3, 3 # Inst8
addi $t4, $t4, -3 # Inst9
beq $t4, $zero, A1 # Inst10
add $t2, $t2, $t3 # Inst11
j A2 # Inst12
A1: addi $t2, $t2, 1 # Inst13
A2: sw $t2, 0($t0) # Inst14
addi $t8, $t8, -8 # Inst15
slt $t7, $t8, $zero # Inst16
beq $t7, $zero, Loop # Inst17
End:

## Slide 43: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped instruction cache: 16 words, 2-instruction blocks.
First instruction (beq) at memory address 0x0040003c.
Assuming beq instruction at Inst10 always branches to A1.
beq $s2, $zero, End # Inst1
addi $t8, $s2, -1 # Inst2
sll $t8, $t8, 2 # Inst3
Loop: add $t0, $s0, $t8 # Inst4
add $t1, $s1, $t8 # Inst5
lw $t2, 0($t0) # Inst6
lw $t3, 0($t1) # Inst7
andi $t4, $t3, 3 # Inst8
addi $t4, $t4, -3 # Inst9
beq $t4, $zero, A1 # Inst10
add $t2, $t2, $t3 # Inst11
j A2 # Inst12
A1: addi $t2, $t2, 1 # Inst13
A2: sw $t2, 0($t0) # Inst14
addi $t8, $t8, -8 # Inst15
slt $t7, $t8, $zero # Inst16
beq $t7, $zero, Loop # Inst17
End:
(e) How many cache hits and misses are there?
No. of instructions = 3 + 51212 = 6147
Index field: 3 bits
Byte offset: 3 bits
First instruction at 0x0040003c
 ...0011 1100
 index 7, 2nd word

## Slide 44: 7.
Arrays A and B each contains 1024 positive integers.
Direct-mapped instruction cache: 16 words, 2-instruction blocks.
First instruction (beq) at memory address 0x0040003c.
Assuming beq instruction at Inst10 always branches to A1.
beq # Inst1
addi # Inst2
sll # Inst3
Loop: add # Inst4
add # Inst5
lw # Inst6
lw # Inst7
andi # Inst8
addi # Inst9
beq # Inst10
add # Inst11
j # Inst12
A1: addi # Inst13
A2: sw # Inst14
addi # Inst15
slt # Inst16
beq # Inst17
End:
(e) How many cache hits and misses are there?
No. of instructions = 3 + 51212 = 6147
Index field: 3 bits
Byte offset: 3 bits
First instruction at 0x0040003c
 ...0011 1100
 index 7, 2nd word
Cache content:
Index
0
1
2
3
4
5
6
7
I2
I3
I4
I5
I6
I7
I8
I9
I10
I11
I12
I13
I14
I15
I16
I1
I17
9 misses: I1,I2,I4,I6,I8,I10,I13,I14,I16.
Therefore 6147 – 9 = 6138 hits.

## Slide 45: End of File